## Slide 1: Rolling Horizon Model for Gasoline Blend Planning under Uncertainty in Demands
Mahir Jalanko, Vladimir Mahalec McMaster University
Department of Chemical Engineering
AICHE 2018, Pittsburgh

## Slide 2: Planning under uncertainty
Uncertainties in production planning problems stem from:
Difficulties in forecasting the future markets:
  The future states are not known exactly (Products demand & prices, raw materials supply & prices)
Measurements:
  The current state is not accurately known (sensor errors)
Unsteady operation:
  Disturbances
Notes: You can talk about how hard it is to make a production plan when future parameters are not fully known due to difficulties in forecasting the future, measurements errors and unsteady upstream operations

## Slide 3: Gasoline blending planning problem
  Objective: Maximize profit
  Constraints:
    Mass balances
    Product Demands
    Blend properties
    Unit process capacity
  Model: Multi-periods, multi-products
  Component production rates are known at each period
  Products demands:
    Contracted demand (certain)
    Additional demand (time-varying uncertainty)
GOAL: Make an optimal production plan over the planning horizon
(how much to produce of each product and when, also production recipes)
Notes: The goal of our model is to make an optimal production plan (when to produce products and by how much) + what recipes ? We need optimal production plan and recipe “recipes are how much to use from each raw material into product)

## Slide 4: Challenges & Motivation
Reasons for uncertainty in products demand:
  Gasoline products demand fluctuation
  Hard to accurately predict market demands for gasoline products in the future
Ignoring demand uncertainty will result in sub-optimal solution:
  Not using optimal blend recipes that correspond to the products demand
  Shortage in production (unmet demand)
Motivation: How can a planner make current period decisions while still considering future uncertain demand

## Slide 5: Model Assumptions
Additional uncertain demand follows normal distribution .
Time varying uncertainty (higher demand variance for periods further into the future)
Fixed-end rolling horizon (uncertain demand updates)
There are eight qualities monitored:
aromatic content (ARO), benzene content (BEN), olefin content (OLF), and sulfur content (SI) are assumed to blend linearly on a volume basis.
(SGI) is assumed to blend linearly on a weight basis.
CASE 1
  Research octane number (RON), Motor octane number (MON), and Rapid vapor pressure (RVP) are assumed to blend linearly
CASE 2
  Research octane number (RON) and Motor octane number (MON) are blended nonlinearly based on ethyl RT-70 models.
  Rapid vapor pressure (RVP) is assumed to blend nonlinearly (linearized by reformulation).
Chart: Additional Demand
Notes: There are two parts of demand contracted and additional, contracted is certain while additional is uncertain.. I assumed that additional demand is predicted to 20% of the contracted demand. The variance of the contracted demand is higher for future farther in the future (its hard to predict accurately when periods are far away into the future). We use fixed end rolling horizon, which means the number of periods decreases by one every time we move forward in time. The graph shows the normally distributed additional demand. I solve the problem using two cases as I stated above (results are for both of these cases)

## Slide 6: Expected Revenue (future periods)
)
) = )
LOSS FUNCTION IN THE OPTIMIZATION MODEL
i = 1-4
Chart: Z
 | 6 | 5.9 | 5.8 | 5.7 | 5.6 | 5.5 | 5.4 | 5.3 | 5.2 | 5.1 | 5 | 4.9 | 4.8 | 4.7 | 4.6 | 4.5 | 4.4 | 4.3 | 4.2 | 4.1 | 4 | 3.9 | 3.8 | 3.7 | 3.6 | 3.5 | 3.4 | 3.3 | 3.2 | 3.1 | 3 | 2.9 | 2.8 | 2.7 | 2.6 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2
C: Products prices
P: Production amount
I: Inventory level
x: demand
μ: demand mean
σ: demand variance
Four 6th order polynomial function to approximate the loss function L(Z)
Li, Wenkai, et al. "Refinery planning under uncertainty." Industrial & engineering chemistry research 43.21 (2004): 6742-6755.
Notes: Revenue is the price (c) times the integral of 0 to infinity of min between (production + inventory, demand). If demand is higher than inventory + production, you can only satisfy P+I so you have lost in sale. The lost in sale is shown as the loss function.. This function need to be implemented in our optimization proeblm so I use approximation done by this paper (they approximate using 4 polynomial of degree 6) (the plot shows that)

## Slide 7: Supply-Demand Pinch / 1
Pinch points delineate intervals where optimal operating conditions and optimal feedstock mix are likely to be constant (if there are no inventory infeasibilities)
Time
Amount
Cumulative demand
Cumulative average production
Pinch point
Notes: If we examine cumulative product demand curves over time and compare them with cumulative average production, we can see that the optimal solution will have pinch points between these two curves.
Decomposition of the production planning is based on the fact that the optimal operating conditions are likely to be constant between the inventory pinch points.
That enables us to construct a two level decomposition.

## Slide 8: Planning Decomposition via Supply-Demand Pinch
Time
Amount
Cumulative demand
Cumulative average production
Pinch point
Castillo Castillo, P.A., V. Mahalec, “Inventory Pinch Based, Multi-scale Models for Integrated Planning and Scheduling: I. Gasoline Blend Planning” AIChEJ (2014), 60 (6), 2158-2178
Notes: At the top level there is a nonlinear planning models with a very small number of periods. Initially they are delimited by the inventory pinch points. This level computes optimal operating conditions.
At the second level is a fine grid LP model, which uses optimal conditions computed at the top level and computes how much to produce in each period for each set of operating conditions.
As a result of this decomposition, we will compute an optimal solution with a small number of distinct sets of operating conditions (operating modes) . In contract, if we solve fine grid multiperiod nonlinear planning problem, we may end up with different operating conditions in each period, in addition to having a difficult computational task at hand.

## Slide 9: Supply-demand pinch based planning DETERMINTIC CASE
Maximize profit subject to:
uncertainty in products demand
blend volume limits
inventory constraint
threshold blend amount
MINLP model with N time periods
HARD TO SOLVE
  (The higher N, the more difficult)
Full space model
Maximize profit subject to
uncertainty in products demand
for K pinch-delineated periods .
(MINLP model with K periods; K << N )
Blend volume computation subject to
inventory constraints .
blend volume limits .
threshold blend amount
(MINLP model with N periods)
Optimize blend recipes
Supply-demand pinch based decomposition
Compute feasible blend plan
Notes: The two approaches to solve the model are full space model which assumes detailed model for all periods and the supply demand pinch which assumes aggregated model (this is what Pedro has done) (deterministic case)

## Slide 10: Fixed-End Rolling Horizon Model
Notes: Here I show how the fixed end rolling horizon model will work

## Slide 11: Fixed-End Rolling Horizon Model UNCERTAINITY IN DEMANDS CASE
Full space model
…
…
Supply-demand pinch model
…
…
t1
t2
t3
T
t1
t2
t3
T
Fixed decisions
t1
K1
t1
t2
k1
Fixed decisions
Current period
Future periods
Past periods
K
K
K periods based on supply-demand pinch
K periods are less than T periods (K << T)
If first infeasibility occurs at:
Period after our current period
resolve the problem with the next period being detailed too
Period further into the future
Subdivide the k periods to two periods at the point where infeasibility occurs
t1
t2
t3
T
t3
Top level
Bottom level
Fix recipes, delivered and blended volumes
where to subdivide if infeasibility occurs
Notes: The full space model assume details plan for current period and future periods, while supply demand pinch model assumes detailed plan for current period and aggregate future periods based on supply demand pinch. If infeasibility occurs we use the rules I list based on if infeasibility show in the next period or in future periods

## Slide 12: Example (MODEL SIZE)
Model | Linear Blending Rules Case |  |  | Non-Linear Blending Rules Case |  | 
 | Full Space | Supply-demand Pinch |  | Full Space | Supply-demand Pinch | 
 |  | Top level | Bottom level |  | Top level | Bottom level
# periods | 14 | 3 | 14 | 14 | 3 | 14
# equations | 4722 | 704 | 3280 | 5142 | 794 | 3280
# continuous variables | 1996 | 344 | 2432 | 2416 | 434 | 2432
# nonlinear terms | 666 | 138 | 78 | 1002 | 210 | 78
# Discrete variables | 420 | 54 | 420 | 420 | 54 | 420
Chart: Periods
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
CTD | 0 | 192 | 348 | 516 | 690 | 858 | 1032 | 1188 | 1422 | 1668 | 1782 | 1896 | 2028 | 2160 | 2400
CATP | 180 | 1668 | 2400
Notes: Here I show the model size for the full space model and supply demand pinch model (the supply demand pinch model compute recipes at the aggregated level then pass them to the bottom level where the feasibility of the recipes are checked)

## Slide 13: Example (RESULTS LINEAR BLENDING RULES CASE)
Chart: Periods
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
CTD | 0 | 192 | 348 | 516 | 690 | 858 | 1032 | 1188 | 1422 | 1668 | 1782 | 1896 | 2028 | 2160 | 2400
CATP | 180 | 1668 | 2400
ANTIGONE 0.001% | FULL SPACE |  |  | SUPPLY DEMAND PINCH |  | 
First Run | CASE 1 | CASE 2 | CASE 3 | CASE 1 | CASE 2 | CASE 3
Revenue | 76333.36 | 76153.93 | 76186.12 | 76333.71 | 76154.21 | 76186.40
Cost | 50968.74 | 50799.85 | 50820.47 | 50969.51 | 50800.56 | 50821.19
profit | 25364.62 | 25354.08 | 25365.65 | 25364.20 | 25353.65 | 25365.21
Execution time | 78.8 | 89.4 | 57.9 | 2.7 | 1.7 | 1.7
Rolling Horizon | CASE 1 | CASE 2 | CASE 3 | CASE 1 | CASE 2 | CASE 3
Revenue | 76242.12 | 76538.95 | 76555.16 | 76242.30 | 76538.95 | 76550.15
Cost | 50925.43 | 51144.54 | 51150.59 | 50925.61 | 51144.54 | 51145.64
Profit | 25316.69 | 25394.41 | 25404.57 | 25316.69 | 25394.41 | 25404.51
Execuation time | 484.8 | 275.6 | 169.02 | 14.3 | 13.9 | 14.5
Notes: You can mention that all models were solved using ANTIGONE solver with optimality gap of 0.001%,The top part represents the solution of the first iteration of the rolling horizon while the bottom represent the solution after finishing rolling horizon for all 14 periods. You can say that top part has tiny difference due to the optimaility gap, while bottom part has difference in solutions in some cases due to both optimality gap and the recipes that used previously can impact the solutions since the use of different recipes in previous periods will get us to different raw materials inventory which might impact the solutions (this shown highly in next slide case 5)

## Slide 14: Example (RESULTS NONLINEAR BLENDING RULES CASE)
Chart: Periods
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
CTD | 0 | 192 | 348 | 516 | 690 | 858 | 1032 | 1188 | 1422 | 1668 | 1782 | 1896 | 2028 | 2160 | 2400
CATP | 180 | 1668 | 2400
ANTIGONE 0.001% | FULL SPACE |  |  | SUPPLY DEMAND PINCH |  | 
First Run | CASE 4 | CASE 5 | CASE 6 | CASE 4 | CASE 5 | CASE 6
Revenue | 76661.91 | 76518.96 | 76556.77 | 76660.91 | 76517.96 | 76556.77
Cost | 51074.76 | 50921.98 | 50945.55 | 51074.76 | 50921.98 | 50945.55
profit | 25587.15 | 25596.98 | 25611.22 | 25586.15 | 25595.98 | 25610.22
Execution time | 176.8 | 163.0 | 221.4 | 7.7 | 2.2 | 7.0
Rolling Horizon | CASE 4 | CASE 5 | CASE 6 | CASE 4 | CASE 5 | CASE 6
Revenue | 76539.43 | 76915.76 | 77140.60 | 76539.43 | 76911.16 | 77140.60
Cost | 51026.74 | 51282.54 | 51476.05 | 51026.74 | 51282.54 | 51476.05
Profit | 25512.69 | 25633.22 | 25664.55 | 25512.69 | 25628.62 | 25664.55
Execuation time | 616.0 | 515.4 | 487.0 | 26.22 | 20.50 | 25.22

## Slide 15: Conclusions
Production plan model that utilizes loss function method was developed to solve the gasoline blend planning under time-varying uncertainty.
The model utilizes fixed rolling horizon formulation that continuously updates the demands predictions of future periods.
When nonlinear blending rules are used to accurately compute the products qualities, the MINLP model resulted is difficult to optimized using commercial solvers for large number of periods.
A two-level decomposition based on supply-demand pinch concept was used to compute solutions in much shorter executions times (around 20 times faster) compared to the full-space model.

## Slide 16: References
Wang, W., Li, Z., Zhang, Q., & Li, Y.: On-line optimization model design of gasoline blending system under parametric uncertainty. In Control & Automation, Mediterranean Conference on (pp. 1-5). IEEE (2007)
Li, J., Karimi, I. A., Srinivasan, R.: Recipe determination and scheduling of gasoline blending operations. AIChE Journal, 56(2), 441-465. (2010)
Jia, Z., Ierapetritou, M.: Mixed-integer linear programming model for gasoline blending and distribution scheduling. Industrial & Engineering Chemistry Research, 42(4), 825-835. (2003).
Castillo, P. A. C., Mahalec, V.: Inventory pinch based, multiscale models for integrated planning and scheduling‐part I: Gasoline blend planning. AIChE Journal, 60(6), 2158-2178. (2014)
Castillo, P. A. C., Mahalec, V., Kelly, J. D.: Inventory pinch algorithm for gasoline blend planning. AIChE Journal, 59(10), 3748-3766. (2013)