## Slide 1
Dr. Adams Group http://PSEcommunity.org/LAPSE:2018.0618
Techno-Economic Analysis of Combining Petroleum Coke and Natural Gas for Efficient Liquid Fuels Production
Ikenna Okeke PhD Student
Dr. Thomas A. Adams II Supervisor
68th Canadian Chemical Engineering Conference
Toronto 2018

## Slide 2: Background
Petroleum coke (petcoke):
  Refinery undesired solid waste
  Up to 40% of heavy oil feed
High petcoke deposits in Canada:
  Jacob Consults: 100 million tonnes (2016)
    Storage limitations
Petcoke disposal:
  Indiscriminate stockpiling
  Environmental concerns
Dr. Adams Group
https://stockbrokernews24.com/6007/global-petroleum-coke-petcoke-market-2018-shell-valero-energy-asbury-carbons-reliance-aluminium-bahrain/

## Slide 3: Motivation
Dr. Adams Group
Petcoke as free fuel source
Instead of stockpiled, clean utilization of petroleum coke
  Gasification to liquid fuels
Reduction in fossil fuel usage
  Displaces some fossil derived fuels
Potential reduced environmental impacts
  CCS technology + fossil fuel displacement
OilChange International 2013

## Slide 4: PSG (Petcoke Only Design)
Dr. Adams Group

## Slide 5: PG-ENGR (Petcoke + External NG Reformer)
Dr. Adams Group

## Slide 6: PG-INGR (Petcoke + Internal Reformer)
Dr. Adams Group
Ghouse, J.H., D. Seepersad, and T.A. Adams, Modelling, simulation and design of an integrated radiant syngas cooler and steam methane reformer for use with coal gasification. Fuel Processing Technology, 2015. 138: p. 378-389

## Slide 7: PG-INGR (Petcoke + Internal Reformer)
Dr. Adams Group

## Slide 8: Heat Exchange Network Design
Dr. Adams Group
CC: Composite Curve
PSG: Petcoke only
PG-INGR: Petcoke + internal reformer
PG-ENGR: Petcoke + External reformer

## Slide 9: Economic Assumptions
Dr. Adams Group
Discounted cash flow rate of return (DCFROR)
  Capacity factor: 85%
Carbon Emission Tax
  $50/tonneCO2
Investment Parameters | Approach
Plant life (yrs) | 30
Construction Period (yrs) | 2.5
Debit/Equity | 80/20
Tax Rate | 40%
Internal Rate of Return (IRR) | 12%
Depreciation Method | MACRS
Operating hours | 8000

## Slide 10: Results: Designs
Dr. Adams Group
Chart: Production rate (ML/y)
| PSG CCS | PSG w/o CCS | PG-INGR CCS | PG-INGR w/o CCS | PG-ENGR CCS | PG-ENGR w/o CCS
Distillate produced | 627.3 | 627.3 | 1025.9 | 1025.9 | 914.4 | 914.4
Gasoline produced | 232.2 | 232.2 | 386.8 | 386.8 | 344.1 | 344.1
Chart: Million USD
| PSG CCS | PSG w/o CCS | PG-INGR CCS | PG-INGR w/o CCS | PG-ENGR CCS | PG-ENGR w/o CCS
Total capital investment | 1117 | 945 | 1382 | 1185 | 1370 | 1163
Net present value | 74 | -589 | 714 | 294 | 489 | -212
Chart: Min Diesel Selling Price ($/gal)
| PSG | PSG | PG-INGR | PG-INGR | PG-ENGR | PG-ENGR
Min. diesel selling price | 1.78 | 2.32 | 1.42 | 1.68 | 1.53 | 1.98
Max. petcoke price | 6.43 | -44.11 | 66.5 | 26.35 | 44.57 | -17.5
PSG: Petcoke only
PG-INGR: Petcoke + internal reformer
PG-ENGR: Petcoke + External reformer

## Slide 11: Results: Emissions & Efficiencies
Dr. Adams Group
Chart: Feed carbon distribution (% mass of carbon)
| PSG CCS | PSG w/o CCS | PG-INGR CCS | PG-INGR w/o CCS | PG-ENGR CCS | PG-ENGR w/o CCS
Carbon in Product | 32.1996 | 32.1996 | 43.6864 | 43.6864 | 38.8857 | 38.8857
Carbon Sequestered | 65.2183 | 0 | 52.8964 | 0 | 58.2484 | 0
Carbon Emitted | 2.5821 | 67.8004 | 3.4172 | 56.3136 | 2.8658 | 61.1143
Chart: Efficiency (HHV%)
| PSG CCS | PSG w/o CCS | PG-INGR CCS | PG-INGR w/o CCS | PG-ENGR CCS | PG-ENGR w/o CCS
Fuel Efficiency (HHV%) | 0.43423 | 0.43423 | 0.51863 | 0.51863 | 0.46169 | 0.46169
Energy Efficiency (HHV%) | 0.33377 | 0.36438 | 0.42558 | 0.44609 | 0.36594 | 0.37861
Chart: GHG Emissions (kgCO2eq/kg)
| PSG CCS | PSG w/o CCS | PG-INGR CCS | PG-INGR w/o CCS | PG-ENGR CCS | PG-ENGR w/o CCS
Direct Emissions | 5.1739 | 135.8211 | 5.0263 | 82.8087 | 4.7607 | 101.4994
Indirect Emissions | 13.5429 | 0.086368 | 18.2944 | 8.4214 | 10.7856 | 6.6744
PSG: Petcoke only
PG-INGR: Petcoke + internal reformer
PG-ENGR: Petcoke + External reformer

## Slide 12: Results: Cost of CO2 Avoided (CCA)
Dr. Adams Group
 | PSG | PG-INGR | PG-ENGR
CCS-Enabled | Yes | Yes | Yes
Total Capital Cost (M$) | 1116 | 1382 | 1370
Annualized Capital Cost (M$/yr) | 294 | 365 | 361
Operating Cost (M$/yr) | 235 | 345 | 315
Total Product (MGJ/yr) | 26.4 | 43.3 | 38.5
Total Product Cost ($/GJ) | 20.1 | 16.4 | 17.6
GHG (kgCO2eq/GJ) | 18.72 | 23.32 | 15.6
CCA ($/tonneCO2eq) | 459 | 237 | 193
= $14.72/GJ
= 30.38 kgCO2eq/GJ
TPC = Total product cost
GHG = Greenhouse gas

## Slide 13: Sensitivity Analysis: Natural Gas Price
Dr. Adams Group
Chart: Natural Gas ($/MMBtu)
| 1.2150000000000001 | 2.4300000000000002 | 3.6450000000000005 | 4.8600000000000003 | 6.0750000000000002 | 7.2900000000000009 | 8.5050000000000008 | 9.7200000000000006 | 10.935000000000002 | 12.15 | 13.365000000000002
PSG with CCS | 109.7018 | 74.2937 | 38.3227 | 2.0181 | -34.7912 | -72.2111 | -110.1327 | -148.6102 | -187.6781 | -227.3548 | -267.6459
PSG w/o CCS | -659.4871 | -588.6592 | -517.8312 | -447.7207 | -381.9021 | -317.6058 | -254.9796 | -194.0345 | -134.734 | -77.0016 | -20.8214
PG-INGR with CCS | 481.4101 | 289.203 | 87.242 | -128.791 | -364.0603 | -622.9715 | -898.9937 | -1175.0159 | -1451.0381 | -1727.0603 | -2003.0825
PG-INGR w/o CCS | 114.6392 | -3.679 | -128.0454 | -259.6642 | -399.0486 | -548.998 | -704.727 | -860.456 | -1016.185 | -1171.914 | -1327.643
PG-ENGR with CCS | 224.4753 | 125.3018 | 22.7011 | -83.636 | -194.5747 | -310.3828 | -431.3765 | -557.7939 | -693.1477 | -828.5015 | -963.8553
PG-ENGR w/o CCS | -321.7446 | -412.7166 | -508.7569 | -608.542 | -708.3271 | -808.1122 | -907.8973 | -1007.6825 | -1107.4676 | -1207.2527 | -1307.0378
Base case Price

## Slide 14: Conclusion
Dr. Adams Group
Different petcoke conversion strategies were evaluated in terms of economics and environmental impacts.
Performance metrics employed were:
  NPV
  MDSP
  Carbon, Fuel, and Energy Efficiencies
Overall, PG-INGR design showed to be a promising technology at current market condition.
Due to the ever-changing market conditions, a flexible PG-INGR configuration needs to be designed to ascertain its performance under uncertainty.

## Slide 15: Acknowledgment
Dr. Adams Group
Supervisor
  Dr. Thomas A. Adams II
Research funding:
  NSERC Discovery grant

## Slide 16
Dr. Adams Group
Thank You
Presentation slides available for download:
http://PSEcommunity.org/LAPSE:2018.0618

## Slide 17: References
Dr. Adams Group
EIA Monthly Energy Review January 2017
BP Statistical Review of World Energy, June 2016
Murthy, B.N., et al., Petroleum coke gasification: A review. The Canadian Journal of Chemical Engineering, 2014. 92(3): p. 441-468.
Jacobs Consultancy, Executive Summary.
Ghouse, J.H., D. Seepersad, and T.A. Adams, Modelling, simulation and design of an integrated radiant syngas cooler and steam methane reformer for use with coal gasification. Fuel Processing Technology, 2015. 138: p. 378-389.
Saharei, 2016 Reduced Order Modeling & Scale-up of an Entrained Flow Gasifier PhD Thesis.
Netzer, D. and C. Wallsgrove, PETCOKE & METHANOL—1: Flow scheme envisions producing methanol for gasoline blending. Oil and Gas Journal, 2011. 109(13): p. 114.
Green, D.W., Perry’s chemical engineering handbook. McGrawHill Professional Publ, 2007.
Boushehri, A., et al., Equilibrium and transport properties of eleven polyatomic gases at low density. Journal of physical and chemical reference data, 1987. 16(3): p. 445-466.
Guevara, F., B. McInteer, and W. Wageman, High‐Temperature Viscosity Ratios for Hydrogen, Helium, Argon, and Nitrogen. The Physics of Fluids, 1969. 12(12): p. 2493-2505.
Latto, B., Viscosity of steam at atmospheric pressure. International Journal of Heat and Mass Transfer, 1965. 8(5): p. 689-720.
Vargaftik, N.B., Handbook of thermal conductivity of liquids and gases. 1993: CRC press.
Uribe, F., E.A. Mason, and J. Kestin, Thermal conductivity of nine polyatomic gases at low density. Journal of physical and chemical reference data, 1990. 19(5): p. 1123-1136
Chase, M.W., Jr., NIST-JANAF Themochemical Tables, Fourth Edition, J. Phys. Chem. Ref. Data, Monograph 9, 1998, 1-1951

## Slide 18: Heat Exchange Network Design
Dr. Adams Group
CC: Composite Curve